## Slide 1: TOPICAL HEMOSTATS , GLUES AND LASERS IN NEUROSURGERY

## Slide 2: Hemostasis in neurosurgery
One of the most important aspects of surgery.
Control of bleeding without ligature
Unlike in abdominal and other surgeries ligatures and packs rarely useful.
Many hours lost in bleeding control

## Slide 3: Topical hemostats
Agents that help in controlling bleeding.
Ideal topical hemostat:
efficacious
minimal or no side effects
affordable
available

## Slide 4: Sources of bleeding
Scalp/muscles
Bone
Dura and sinuses
Brain:capillary/venous/arterial.

## Slide 5: Topical hemostats
Microfibrillar collagen
Thrombin
Fibrin glue
Hydrogen peroxide(3%)
Surgicel
Oxycel
Gelfoam
Surgicel Fibrillar
Bone wax
cottonoids
Mechanical
Chemical

## Slide 6: Surgicel
Surgicel (Ethicon) is an oxidized cellulose polymer (the functional unit is poly anhydroglucuronic acid) formed by dissolving pure α-cellulose (plant derived) in an alkaline solution.
Introduced in 1940s.
It is then regenerated into continuous fiber, knitted into gauze, and oxidized.
Applied dry, absorbs within 4 to 8 weeks.
Forms a brownish or black gelatinous mass in contact with blood.

## Slide 7
Oxycel (Becton Dickinson) is another oxidized cellulose polymer product that is similar.
Surgicel is composed of solid fibers with irregular contours on cross-section, whereas Oxycel is composed of hollow “twisted tubule” fibers.

## Slide 8: Surgicel………
Acts as a physical matrix to which platelets can adhere which, in turn, aids in clot formation
Additional pressure of the mass also contributes to the haemostatic process.
Relatively bacteriostatic because of its relatively low pH, it deactivates and denatures some of the bacterial proteins thus making them more susceptible to antibiotics.
Needs to be applied dry.

## Slide 9: Gelatin sponge(Gelfoam/surgifoam)
Introduced in the 1940s for neurosurgical procedures.
Derived from purified pork skin gelatin.
Absorbs approximately 45 times its weight in blood and can expand to approximately 200% of its initial volume.
Can be used dry or saline soaked.
Absorbed in approximately four to six weeks.

## Slide 10: SURGICEL Fibrillar
oxidized regenerated cellulose(1969)
Layers can be peeled off in desired amounts.
conforms to irregular surfaces, even hard-to-reach areas
surgical visualisation is improved by ability to cauterise directly through it
fully absorbed within 14 days

## Slide 11: Microfibrillar collagen(Avitene)
Collagen which is derived from bovine skin. binds tightly to blood surfaces.
Causes minimal swelling especially when compared to Gelfoam .
In addition to being collagen and causing contact activation, it does somehow directly activate platelets with subsequent aggregation.
May reduce the number of free platelets in normal individuals .
Loses effectiveness in thrombocytopenia(<10,000).
It is absorbed in 3 months and needs to be applied dry.

## Slide 12: Thrombin(thrombostat/thrombinar)
Thrombin directly activates fibrinogen and converts it into fibrin monomers.
Can be used directly or combined with gelatin sponge
Produced from bovine prothrombin hence antigenic.
If injected into large vessels can lead to thrombosis and complications.

## Slide 13: Complications
Nidus of infection
Inflammatory reaction(esp. avitene)
Antigenicity(animal products)
Mass effect(esp.gelatin)
Gossipiboma

## Slide 14: Bone wax
Pioneered by Sir Victor Horsley(1892).
  Horsley’s wax: bees wax, 7 parts; almond oil, 1 part; salicylic acid, 1 part.
Modern wax:88% refined beeswax and 12% isopropyl palmitate (softening agent)
Effective in controlling bleeding from bone
Once smeared across the bleeding edge, immediate hemostasis occurs.

## Slide 15: Complications
1) Bone wax inhibits osteogenesis
2) Increases infection rates (the number of bacteria needed to produce osteomyelitis is reduced by a factor of 104 (10,000)
3) Remains as a foreign body for many years

## Slide 16: Ostene
Sterile mixture of water-soluble alkylene oxide copolymers.
Inert artificial material feels and works like wax.
Does not increase infection rates, does not interfere with bone healing, and is non-inlfammatory.

## Slide 17: Fibrin glue(Tisseel/crosseal)
Commercially available/autologous.
2 components:
a)fibrinogen, factor13, fibronectin, aprotinin, plasminogen, cryoprecipitate
b)thrombin and calcium
After mixing, fibrinogen is converted to fibrin
Aprotinin inhibits premature fibrin degradation

## Slide 18: Uses
For hemostasis and tissue sealing
To establish hemostasis
To reinforce dural closure and prevent CSF leak.
In anastomosis of nerves and nerve grafts
(Micro neural anastomosis with fibrin glue : an experimental study. Suri A, Mehta VS, Sarkar C .Neurology India.2002)
Fixation of bone fragments to repair skull defects.

## Slide 19: Lasers in Neurosurgery
LASER(Light Amplification by Stimulated Emission of Radiation)
Precise means of incision and coagulation of biological tissues.
Each Laser medium has specific wavelengths and hence different absorption, penetration and scatter.
Carbon dioxide(10.6micrometre),Argon
(4888nm),Nd:YAG(1060nm)

## Slide 20: Uses
Removal of extra axial tumors in sensitive areas.
Neuroablative procedures (cordotomy, myelotomy etc)
Vascular neurosurgery.
Laser discectomy.

## Slide 21: Conclusion
Proper surgical principle remains the key.
Judicious use of haemostatic agents is advised.