## Slide 1: TRANS CRANIAL DOPPLER

## Slide 2: Transcranial Doppler
1982, Aaslid and colleagues introduced TCD as a non-invasive technique for monitoring blood flow velocity in basal cerebral arteries in patients with SAH
Now increasingly used in intensive care units and anesthesia for research and clinical practice

## Slide 3: Doppler Effect
1842, Christian Doppler - frequency shift of reflected and scattered signals that occurs whenever there is relative motion between the emitter and the object or interface reflecting the sound

## Slide 4: Principles
Uses a handheld, directional, microprocessor-controlled, low-frequency (2-MHz), pulsed doppler transducer to measure the velocity and pulsatility of blood flow within the arteries of the circle of Willis and vertebrobasilar system
Noninvasive, nonionizing, portable, inexpensive, safe for serial or prolonged studies

## Slide 5
Based on detection of frequency shifts from insonated RBC moving through a small preselected arterial spatial region (sample volume).
Sample volume is determined by lateral focussing of the transducer, duration of transmitted sound burst at a specific pulse repitition rate (PRF) and duration of the range gate opening (Ts)

## Slide 6: History
1979, Nornes described the intraoperative pulsed doppler sonographic method to study cerebral hemodynamics
1982, Aaslid et al introduced the 2 MHz pulsed doppler device that enabled the noninvasive transcranial measurement of blood flow velocity in large intracranial basal vessels

## Slide 7
1986, Eden Medical Electonics developed the Trans-scan, device capable of three dimensional, multiprojectioal flow mapping, colour coded for flow direction and velocity
1988, EME introduced the TC20005 scanner, TCD with advanced post-processing and display capabilities
Recent developments- introduction of intravascular sonographic contrast agents, multi-channel transcranial doppler

## Slide 8: Examination Technique
Can be performed in any patient- awake or comatose
Four naturally occurring cranial windows
  Transtemporal- 3 windows
  Transorbital
  Transforaminal
  Submandibular
  In addition- open fontanelle, burr holes

## Slide 9
WINDOWS
A.Transtemporal,
B. Transorbital
C. Transforaminal,
D. Submandibular

## Slide 10
Criteria for Vessel Identification
1 . Cranial window used
2. Depth (mm) of sample volume
3. Direction of flow (toward or away from transducer, bidirectional)
4. Distance (mm) over which vessel can be traced without branching
5. Relationship to TICA/MCA/ACA junction
6. Angle of transducer in relationship to patient’s head and cranial windows
7. Relative flow velocity (MCA > ACA > PCA = BA = VA)
8. Response to common carotid artery compression

## Slide 11: Angle of insonation
Angle between the ultrasound beam and the vessel being recorded from
Important to measure true TCD velocity
Observed velocity = True velocity X cosine of angle of insonation

## Slide 12
Vessel Identification Criterion
Vessel Window Depth Direction Velocity
MCA TT 45-65 Toward 46-86
ICA Bifur TT 60-65 Bidirectional
ACA TT 60-75 Away 41-76
PCA 1 TT 60-75 Toward 33-64
PCA 2 TT 60-75 Away 33-64
Ophthalmic TO 45-60 Toward 21-49
ICA (supra- TO 60-75 Away 50-60
clinoid)
Vertebral TF 65-85 Away 27-55
Basilar TF 90-120 Away 30-57

## Slide 13: Pulsatility
Described by the shape of the spectral waveform
Relates to the peripheral resistance of the cerebral tissue supplied by the insonated vessel and the input signal
Normal Vs> Vd
High pulsatilty Vs>>Vd
Damped pulsatility Vd > 50% of Vs

## Slide 14: Pulsatility Index
Gosling Equation
PI = Vs – Vd/ Vm
Normal = 0.8- 1.2
Increased > 1.2, seen in Increased ICP, hypocapnia, aortic insufficiency, bradycardia
Decreased < 0.8, seen in vessel supplying AVM due to decreased peripheral vascular resistance, downstream high grade stenosis

## Slide 15: Physiologic factors affecting TCD
Age
Sex
Hematocrit
Temperature
Hypoglycemia
Blood CO2 level
Cardiac Output
Brain Activity

## Slide 16: Use in Neurosurgery and Anesthesia
Intracranial and extracranial Vascular Abnormalities
  Intracranial
    SAH and Vasospasm
    Head Injury
    Arteriovenous Malformation
    Arterial stenosis and Occlusion
    Detection of aneurysm
    Brain Death
  Extra cranial
    Subclavian steal Syndrome
    Carotid Stenosis
    Positional Vertebral artery Occlusion

## Slide 17: Use in Neurosurgery and Anesthesia
Intraoperative and procedural Monitoring
  Carotid Endarterectomy
    For cross-clamp Hypoperfusion
    Detection of emboli
    Postoperative hyperperfusion
    Postoperative occlusion
  Cardiopulmonary Bypass

## Slide 18: SAH and Vasospasm
Most accurate in MCA
Velocity > 120 cm/s = Vasospasm
> 200 cm/s = Severe Vasospasm
Velocity Increase > 50 cm/S over 24 hour period – high risk for DIND
D/D vasospasm and Hyperemia
Lindegaard Ratio
VMCA/VICA ( 1.7 ± 0.4)
> 3 = vasospasm

## Slide 19
Monitoring response to Tripple H therapy, Endovascular therapy
Detection of Intracranial Aneurysm – introduction of trans-cranial colour coded sonography
Peroperatively can be used for assessing the vasospasm, patency of vessels, residual aneurysm

## Slide 20: Head Injury
Blood flow velocity from relative flow changes- Vasospasm/ Hyperemia
CO2 reactivity
Cerebral Autoregulation
    Static autoregulation
    Dynamic autoregulation
Post-traumatic Vasospasm
Vascular Dissection

## Slide 21: Brain death
False positive
  Cerebral circulatory arrest can be transient
  Residual brainstem circulation
  Abnormally low diastolic pressure; IABP
False Negative
  Complete destruction of brainstem with preserved supratentorial flow

## Slide 22: Arteriovenous Malformation
High velocity in feeding arteries
Low pulsatility index s/o decreased peripheral vascular resistance
Defective autoregulation
Intraoperative use to detect residual aneurysm during surgery or neuroendovascular procedures

## Slide 23: Intraoperative and Procedural Monitoring
Carotid Endarterectomy
    For cross-clamp Hypoperfusion
    Detection of emboli
    Postoperative hypoperfusion
    Postoperative occlusion

## Slide 24: During Cardiopulmonary Bypass
Dynamic evaluation of cerebral blood flow
Detection of emboli during aortic cannulation and cardiac manipulation

## Slide 25: Latest development
Transcranial colour coded Ultrasonography
f-TCD