## Slide 1: DIFFUSION TENSOR IMAGING AND TRACTOGRAPHY

## Slide 2: Introduction
Diffusion- random molecular motion also known as Brownian movement
Biological systems depend on diffusion for normal functioning like diffusion of metabolites into the cell.

## Slide 3: Introduction
Diffusion MRI- Produces in vivo images of biological tissues weighted with the local microstructural characteristics of water diffusion.
based on
2 types- DWI and DTI based on isotropy and anisotropy

## Slide 4
Isotropy- symmetrical diffusion in all directions
Anisotropy- asymmetrical diffusion in different directions

## Slide 5: DWI
Most applicable when the tissue of interest is dominated by isotropic water movement
  Eg- grey matter and major brain nuclei
DTI
  Most applicable when the tissues have a highly organised structure and hence diffusion is anisotropic because of barriers
    Eg- Neural axons- myelin forms important barrier

## Slide 6: Terminologies
1) Eigen values- ƛ1, ƛ2, ƛ3- to quantify the diffusion in three orthogonal directions
2) Fractional anisotropy- The anisotropy is expressed relative to the magnitude of diffusion.
FA values ranges from 0 to 1( 0- isotropic and corresponds to a perfect sphere
1- anisotropic diffusion and corresponds to ideal linear diffusion)
3) Mean Diffusivity (ADC)- average of the three eigen values

## Slide 7: Tractography
A technique used to demonstrate the white matter tracts
Uses DTI sequence.
The number of fibres and degree of anisotropy have a direct relationship

## Slide 8: Colour coding of tracts
RED- Directions in x axis ( left-right)
GREEN- Y axis ( Posterior to anterior)
BLUE- z axis ( Superior to inferior)
Colour- direction of greatest diffusion
Brightness- degree of anisotropy

## Slide 9: Applications
Traumatic brain injury-DAI
Assessment of the morphology of tracts in lesions adjacent to eloquent areas of brain
Spinal disorders-
  Acute and chronic spinal cord compression
  Spinal cord tumours- characterisation
  AV malformations
  Syringomyelia
Alzheimer’s disease

## Slide 10: DTI in TBI
Reliable tool for in vivo quantification of white matter microstructural alterations following TBI
They provide valuable information about the axonal integrity and function
Useful for the identifying the early signs of axonal injury in TBI

## Slide 11
Studies on DTI state that it is a clinically relevant biomarker in TBI
Tool for revealing the changes in neural tissue during recovery

## Slide 12
Also useful in assessment of severity of DAI
Can have a bearing on functional outcome and ? therapeutic impact.