## Slide 1: INTRAOPERATIVE ULTRASOUND IN NEUROSURGERY

## Slide 2: MYTHS
Image Quality: ?inferior to MR
Minimally invasive surgery incompatible: ?need for bigger craniotomies
No use at end of surgery?, decline in image quality
US interpretation ?difficult than MR

## Slide 3: History
French et al. – 1950
(A Mode – experimental studies on brain tumor)
Leksell- 1954 , SDH localization, later Echoencephalogram
Wild and Reid – 1978

## Slide 4: Physical Principles
Reflection- most important for image buildup
Absorption
Scattering
Artifacts

## Slide 5: Image Buildup
Frequency :
High frequency(10MHz)- high resolution, less penetration and vice versa
Focus : Beam – narrowing- higher resolution
Depth : Deeper gives more overview.
AIM – to achieve resolution 25 um at 50 MHz
Notes: Surfcae lesion < 15 mm cortex 10Mhz, Focus 20 mm, depth 40 mm max….
Deep lesion 5 Mhz, Focus 50 mm, depth 70 mm

## Slide 6: Machine considerations
Modes *ABCD
Storing features
Transducers *
Financial considerations

## Slide 7: Modes
A Mode- amplitude mode, depth measurement
Uses:
Seldom used
Focused beam for calculi Rx
B Mode- Brightness mode(real time gray scale display >18fps)
Uses:
Real time imaging
Widely used

## Slide 8: Modes
C Mode– Color mode
- All moving particles encoded with different red and blue shades
- Velocity and direction dependent
Uses: Blood flow/vessels detection
D Mode- Doppler/power/ angio mode
- amplitude of moving structures
Uses : small/slow flow vessels display

## Slide 9: Terminology
1. Echogenicity
Depends on – Reflections of tissue
Anechogenicity : No echogenicity(ventricle)
Low Echogenicity: Normal white matter
High Echogenicity: Glioma
Hyperechogenicity: calcifications/bone- meningiomas

## Slide 10: Terminology
2. Homogeneity
Homogenous- low grade gliomas
Inhomogeneous - high grade glioma
3. Demarcation
Infiltrative v/s Non infiltrative tumors and extent of resection.
Notes: Inhomogenous- with different echoic parts- high grade gliomas

## Slide 11: Artifacts
BLURRED IMAGE
Source: Bubbles trapped at contact surfaces
Brain- sheath
sheath- probe interface
REVERBERATIONS
Source: brain spatulas,
SHADOWING
Source: calcifications
Increased ECHOGENICITY
Source: cysts in front of structures

## Slide 12: Transducers
Linear array and Convex array- Not useful
(convex interface and poor resolution)
Phased array- widely used
BEST- small phased rectangular acoustic lens and area of contact 20-25 mm

## Slide 13: Transducers- suited in NSx
Phased array
Burrhole transducer
Convex array

## Slide 14: Sterilization
Not suited
Sterile sheath to be used

## Slide 15: Getting started
First locate sulci/interhemispheric fissure to gain orientation

## Slide 16: Applications
Mass Lesions localization
Inflammatory and Infectious disorders
AVM
Burrhole /guided biopsies
VP shunt
Aneurysm
Neuronavigation

## Slide 17: MASS LESION LOCALISATION- cranial
All tumors Hyper echoic,
except- cystic components and Lymphoma(iso to hypo echoic)
Surrounding parenchyma and vasogenic edema – relatively hypoehoic
PITFALLS- Chronic edema /radiation changes may change echogenicity. Wrong orientation over gyrus

## Slide 18: Cranial Uses
Resection control
To delineate tumor vascularity
Localizing site for biospy
Minimally invasive hematoma drainage
Aspiration of abscess and cysts
Patency of arterial bypasses

## Slide 19: MASS LESION LOCALISATION- cranial
Vascularity assessment- Colour duplex sonography – B mode with color mode
High grade glioma, in relation to vessels

## Slide 20: Resection control
Thalamic tumor in sagittal and coronal planes, with gradual excision. At end of resection residual seen And was resected further to achieve sonograhic total excision

## Slide 21: MASS LESION LOCALISATION- Spinal
Normal spine
Dura: Echogenic ring with surrounding anechoic CSF
Spinal cord: homogeneous low-level echoes, demarcated from CSF by bright echogenic line
Central canal: echogenic structure
Nerve roots: echogenic

## Slide 22: MASS LESION LOCALISATION- Spinal
Mass Lesions characteristics:
Cyst/syrinx- anechoic
IM tumor- complex cystic and solid
IM neoplasms - inhomogenous hyperechoic
(glioma, metastases)
Calcifications enhance echogenicity
(ependymoma, astrocytoma, dermoid)

## Slide 23: MASS LESION LOCALISATION- Spinal
Mass Lesions characteristics:
- Focal cord expansion and obliteration of the
central canal
- Extramedullary lesions are generally hyper-echoic (disk, hematoma, meningioma, neurofibroma, bone , cyst abscess)

## Slide 24: Spinal Uses
Syrinx- localize site of needle insertion/ perforation
Tumor biopsy
Myelotomy in avascular planes
Tumor resection

## Slide 25: Neuronavigation
3D USG : By tilting the ultrasound probe over the area of interest, a collection of 2D ultrasound images is acquired, forming a 3D ultrasound image volume
Camera indentifies position of the patient reference frame and the US probe and enables display with corresponding preop MR
Time taken ~ 1 min

## Slide 26: Neuronavigation
Accuracy of 3D US
Preop MR may not predict intraop brain shifts
Image to patient registration is not needed for navigation based on intra-operative US
Acquisition is performed in the same coordinate system as navigation is executed.
New 3D images can be acquired in order to compensate for brain shift

## Slide 27: Other procedures : Biopsy
Free hand
USG transducer mounted biospy probe
Diagnostic yields of 85-100% reported in literature-
Depth and nature of pathology
Most hyperechoic region to be chosen

## Slide 28: Other procedures : VP shunt
Special burrhole transducer < 12mm diameter
use of separate burrhole/ larger burrhole, in open fontanelle

## Slide 29: Cavernoma
Hyperechogenicity
Inhomogeneous- microcalcification, cysts, thrombosis
Demarcation- may be be sharp (cause- iron ring)
Difficult to identify flow in cavernoma

## Slide 30: Venous anomaly
Criteria:
- slow flow (<5 cm/s)
- flow away from lesion
Other cerebrovascular parameters:
Peak systolic flow (AVM >300 cm/s), diastolic flow
Resistance index (<0.6- AVM)

## Slide 31: Other procedures : AVM
Intra-operative 2D colour-duplex-sonography for localizing deep-seated AVMs,
Identifying feeders and draining vessels and for re-section control
Colour Doppler : measure the cerebrovascular resistance and differentiate between feeding vessels and en passant vessels.

## Slide 32: Other procedures : AVM
Stereoscopic display or a 3D rendering of the vessels may be helpful to understand the tortuous architecture of the feeding vessels
Image quality and details inferior to MR
ROLE- to estimate shifts and correction and vessels of nidus

## Slide 33: Other procedures : Aneurysms
2D US for peripheral aneurysms
Flow evaluation in distal vessels pre and post clipping (systolic flow, RI)
PITFALL: Power Doppler of smaller vessels generates smeared image for navigation
ROLE: not clearly defined and needs improvement

## Slide 34: Other procedures : decompression
USG to assess need for duraplasty in Chiari I patients after foramen magnum decompression
ROLE: ? Paradigm shift
CSF related complications v/s No duraplasty
Recurrence rates of symptoms twice in moderate and severe cases in bony decompression only patients-
Mcgirt et al. JNS- pediatrics, July(1) 2008

## Slide 35: LIMITATIONS
Operator Dependent
Requires knowledge of neuroradiologic abnormalities that are not routinely evaluated by sonography.
Difficulties in distinguishing a tumour from normal tissue and lesion obscuration by chronic edema.
CT stereotaxis and real-time MRI fusion images.

## Slide 36: Future
1.5D probe
- thinner image planes at a wider depth range.
- improve the quality of both tissue imaging and
angiography based on power Doppler

## Slide 37: Future
Contrast:
- Thin-shelled micro bubbles (size~RBCs) very strong scatterers of ultrasound
- Size 1-4 um, coupled to galactose, albumin (albunex, levenist)
Administered iv
Increase signal to noise ratio

## Slide 38: Future
Strain imaging:
- Elasticity of brain tissue.
Tissue motion of arterial pulsations can US strain images of brain tumors
(histologic clue)
Adjunct to B mode
STATUS- under evaluation

## Slide 39: Future
HIFU
- Under evaluation for tumor
- MR guided

## Slide 40: USG AIIMS
B- K medical, equipped with linear(vascular), burrhole, convex array
Surgeries
Foramen magnum decompression
Intracranial tumor excision
Spinal IM tumor localization
Biopsy

## Slide 41: USG – INDIA: PNDT act
The Pre-natal Diagnostic Techniques Regulation and Prevention of Misuse) Act (1994), 1st January, 1996 enacted
Amendment 2003
Restricted use of USG for prenatal diagnosis of sex

## Slide 42
THANK YOU